## Slide 1: Online power management with Quality-of-Service Consideration for Bluetooth Low Energy
Prof. Ya-Shu Chen
Jing-Ho Chen
Notes: 對於無線感測網路系統下 Qulaity of Service 在BLE 中power management上的議題

## Slide 2: Introduction
● Intelligent sensor network
-Sensing information
-Real-time monitor
● Application
- Body sensor network
- Military
- Industry monitor
Predictive Maintenance
Healthcare
Intelligent Buildings
Notes: 現今智能體系(居家 & 城市) 已漸漸展開，立即性的吸收到周遭感測訊息與監控控制議題也越來越多人探討，若要組織如此龐大的體系上
感測節點就佔有一席重要地位，需要能監控周圍資訊、處理且回傳做監控，這些流程對於感測器來說是基本過程
(就我們熟知的感測器(小米 jawbone)是具有感測人生裡資訊且能回傳資料給使用者觀看)
http://www.ithome.com.tw/news/97980
https://smartcitizen.me/pages/smartcitizen
一個完整的物聯網體系需具備三個要素，分別為感知、傳輸及智能處理
無線嵌入式裝置的需求性
感測需求量擴增
無線傳輸必要性
2015/8/11
這個智慧市民感測裝置（Smart Citizen Kit，簡稱SCK）是由歐盟贊助推動的一項智慧城市計畫，”阿姆斯特丹”在去年3月發表了第一版市民感測裝置，提供免費的感測裝置讓市民帶回家。
目前在全球各地區布建了1,187個裝置，將近6千個感測器，累積5千萬筆資料，所有資訊都被即時傳送到線上資料平臺。

## Slide 3: Motivation
● Real-time
- Emergency treatment
- Real time hardware
● Battery capacity
-Varied applications data rate
-Power consumption (Transmission power)
http://www.ti.com/lit/ug/swcu117d/swcu117d.pdf [CC13xx, CC26xx SimpleLink™ Wireless MCU Technical Reference Manual]
Notes: Radio上的耗能尤為嚴重，所造成的radio consumption有許多的設計上的solution
因此我們選用BLE最佳的傳輸方案來做為我們的傳輸protocol

## Slide 4: BLE Protocol
● Bluetooth Low Energy (BLE)
- BLE is designed to reduce power consumption and merged into Bluetooth standard
in 2010.
- The distance between two connection events for notifying each status is called
connection interval.
http://www.summitdata.com/blog/ble-overview/
Chart: Avg Current with interval
Chart: Avg Current with interval
Notes: 說出重點，且舉出非線性
遇到問題
-單一節點上connection interval調整 <Application>
-Star 上的問題 (send-and-confirm)
-Mesh propose

## Slide 5: Star Topology
●Connection interval assignment
-Master-Slave architecture
-Synchronization
-Collision constraint
Master
Slave1
Slave2
Connection interval of Slave1
Connection interval of Slave2
5
Master
Slave1
Slave2
Collision Problem
Master
Slave1
Slave2
Slave3
●Assign interval with multiple devices
-There is only one master to manage the multiple sensing data from multiple slaves.
-The multiple slaves need to be synchronize with master and master should wait only
one device at one time.
-In the multiple slaves, there has the collision constraint without write-request scheduler.
Notes: Collision Master buffer會被erase

## Slide 6: Problem
● Proposal
- We propose the MEI to assign service interval for device with varied data rate.
- We propose the EIMA to prolong lifetime of network with collision constraint.
- We propose the EIF to raise quality-of service in wireless sensor network.
● Constraint
-Varied application rate
-Collision constraint
● Goal
-Maximize sensor network lifetime
Notes: BLE上針對real time的問題
Message latency調整interval
Conflict issue切割傳輸時間<否則會loss packet>

## Slide 7: Related Work
Ref[1] proposed the real-time scheduling to evaluate which one between the Bluetooth and IEEE 802.15.4 suitable for the industrial process systems.
Ref[2] presents the strategy to minimize number of retransmission overhead for supporting real-time and reliable.
[1] Collotta, Mario, Giovanni Pau, and Gianfranco Scatà. "Deadline-aware scheduling perspectives in industrial wireless networks: A comparison between IEEE 802.15. 4 and Bluetooth." International Journal of Distributed Sensor Networks 2013 (2013).
[2] Zhu, Xiuming, et al. "Mbstar: A real-time communication protocol for wireless body area networks." Real-Time Systems (ECRTS), 2011 23rd Euromicro Conference on. IEEE, 2011.
● Real time
Notes: [1]Bluetooth來做real-time schedule於real-time的環境下， (提出 bluetooth 比上IEEE 802.15.4更適合用於real time議題上)
不同點: 沒有考量varied data rate情況下且不具有energy saving上的議題
[2]考量在real-time議題下的WSN運用EDF & RM schedule來達到retransmission次數縮減
不同點為: 沒有考量energy balance 來達到lifetime延長，且沒有考量collision

## Slide 8: Related Work
Ref[3] determines the smallest length conflict tree for decreasing the latency in the WSN.
Ref[4] proposes sleeping schedules for contention and polling access schemes to extend the device lifetime.
Ref[5] proposes the novel power-management framework for BLE by scaling the connection interval during runtime.
Ref[6] presents the DIF in EDF scheduling to adjust the transmission rate with arbitrary individual deadline for minimizing the energy consumption.
[4] Jacob, Anil K., and Lillykutty Jacob. "Energy Efficient MAC for QoS Traffic in Wireless Body Area Network." International Journal of Distributed Sensor Networks 2015 (2015).
[5] Doudou, Messaoud, et al. "Duo-MAC: Energy and time constrained data delivery MAC protocol in wireless sensor networks." Wireless Communications and Mobile Computing Conference (IWCMC), 2013 9th International. IEEE, 2013.
[6] P. Kindt, D. Yunge, M. Gopp and S. Chakraborty, “Adaptive online power-management for Bluetooth Low Energy”, IEEE Conference on Computer Communications (INFOCOM), 2015
[7] F. Shan, J. Luo, and X. Shen, “Optimal energy efficient packet scheduling with arbitrary individual deadline guarantee,” Compute. Netw., vol. 75, pp. 351–366, Dec. 2014
● Transmission rate
● Write-request schedule
Notes: Write-request scheduling
[3]以TDMA方式做collision avoid的問題，以最少的排列方式，減少傳輸時間上的消耗
不同點: 沒有energy上的節能
[4]在body sensor network環境下，做polling輪詢方式輪流詢問，目標為提升lifetime [運用設定各個node上的priority來做輪詢並且校正sleep time]
不同點: 雖然有energy saving 但未有real-time議題
Transmission rate
[5] 提出的BLE connection interval scaling framework, 針對energy consumption
不同處:沒有考量multiple node情況 沒有real time議題
[6] 提出間格調整rate方法，根據aperiodic task來做間格性調整
不同處: 沒有考量multiple node情況

## Slide 9: System Architecture
Multiple Event Energy Efficiency Interval (MEI)Estimating the service interval for each node.
Energy Efficiency Interval Multiple Access (EIMA) Estimating the connection interval for each node in WSN.
Earliest Interval First (EIF) Scheduling each node to receive the sensing data.
EIF
Slave1
Slavem
Load1
Period1
Application Event
Loadm
Periodm
Application Event
MEI
EIMA
Connection Interval
Connection Interval
Slave1
Slavem
Master
Notes: 系統架構中包含…(MEI) (EIMA)
之後緊接著為網路的架構圖

## Slide 10: Service Interval
●Assign Interval
-Without data rate consideration
●Assumption
- In the follow example, we assume that there are two packets could be sent for one connection event.
Input | 
Slave | Pkt1(20bytes, 1s) Pkt2(20bytes, 1s) Pkt3(20bytes, 2s)
Inteval1s
Inteval0.1s
Minimum period as interval 1s
Minimum interval0.1s
MISS
●Assign Interval
-In the default setting for interval, it doesn’t consider the sensor sample rate and energy consumption.
●Assumption
- In the follow example, we assume that there are two packets could be sent for one connection event.

## Slide 11: Proposal (Service Interval)
● Multiple Event Energy Efficient Interval (MEI)
-Service interval with varied data rate
● Algorithm
-Demand packets (Periodic event)
-Supply packets (Particular connection interval)
The packet set, included the period of each packet is not bigger than
Demand packets
Supply packets
Parameter | Description
 | Load of i th application
 | Maximum data byte of packet
S | The maximum period in
pi | Period of i th application
D | Service interval
 | Maximum number of packet for one event
 | Testing packet set and ordering by period
Parameter | Description
 | Load of i th application
 | Maximum data byte of packet
S | 
pi | Period of i th application
D | Service interval
 | Maximum number of packet for one event
 | Testing packet set and ordering by period
Notes: S & 要提及
S & Θ要提及

## Slide 12: MEI Example
●Service Interval
-Demand packet v.s. Supply packet
Input | 
Slave | Pkt1(20bytes, 1s) Pkt2(20bytes, 1s) Pkt3(20bytes, 2s)
=1s
=2s
Notes: 最後要repeat
因此在我們的方法會考量各個sensor node上data rate議題，進而達到省能且提供優良的quality
Single node上會考量data rate議題，若擴展成multiple node型態 就會有blocking time上的問題點

## Slide 13: Proposal (Star Interval)
● Energy Efficiency Interval Multiple Access (EIMA)
-To prolong lifetime with collision problem.
Parameter | Value | Description
 |  | Connection event current
 |  | Connection event duration
 |  | Sleep current
 |  | Service interval of i th node
 |  | Connection interval of i th node
Parameter | Value | Description
 |  | Connection event current
 |  | Connection event duration
 |  | Sleep current
 |  | Service interval of i th node
 |  | Connection interval of i th node
Consider to lifetime
Consider to each slave
Chart: Sevice interval (ms)
W1
W2
W3
Notes: 補圖片
(加入decrease程度 圖)

## Slide 14: Proposal (Star Interval)
● Energy Efficiency Interval Multiple Access (EIMA)
Parameter | Value | Description
 |  | Connection event current
 |  | Connection event duration
 |  | Sleep current
 |  | Service interval of i th node
 |  | Connection interval of i th node
Parameter | Value | Description
 |  | Connection event current
 |  | Connection event duration
 |  | Sleep current
 |  | Service interval of i th node
 |  | Connection interval of i th node
 | Service Interval | W | C
Slave1 | 1000ms | 0.02306 | 530ms
Slave2 | 2000ms | 0.01203 | 553ms
Slave3 | 3000ms | 0.00835 | 576ms
Slave1
Slave2
Slave3
Notes: proglong lifetime with collision constraint

## Slide 15: Proposal (Write-Request Scheduler)
● Write-Request Schedule
-Implements table order to notify device.
● Earliest Interval First Schedule (EIF)
- Period of slave (Service Interval by MEI)
- Interval of slave (Connection Interval by EIMA)
- EDF scheduler
- Decision equation
Arrival
Deadline
Arrival
Deadline
Notes: 預測是否會被其他slave block
dn1/cn1 >>> d1時間內會來幾次*cn1 >>>下次來的時間 >>> 看是否小於 t + cn3(目前) >>> 即可知會不會被block

## Slide 16: Example
Input | 
Slave1 | Pkt1(10bytes, 100ms) Pkt2(10bytes, 200ms)
Slave2 | Pkt1(10bytes, 500ms) Pkt2(30bytes, 500ms)
Slave3 | Pkt1(10bytes, 1000ms) Pkt2(10bytes, 1000ms) Pkt3(10bytes, 1000ms)
MEI | 
Slave1 | =100ms
Slave2 | =250ms
Slave3 | =500ms
MEI | 
Slave1 | 
Slave2 | 
Slave3 | 
EIMA |  | 
 | Waiting Time | Period (MEI)
 | 62ms | 100ms
 | 62ms | 250ms
 | 63ms | 500ms
Slave1
Slave2
Slave3
248
249
miss
Master
Slave1
Slave2
Slave3

## Slide 17: Experiment
● Setting
- Input: Data rate is near 80bytes/s-440bytes/s for each device
Sample period is near 200ms, 400ms and 800ms
- Topology: Star topology (3 slave nodes)
- Single node interval: MEI (v.s. Lazy[1], DIF[2], and Greedy)
- Scaling interval in network algorithm: EIMA (v.s. LDC[3], and Greedy)
- Write-request schedule: EIF (v.s. Polling[4], Round Robin, and NPEDF[5])
● Performance Evaluation
-Meet ratio: Evaluate the ratio of meet packet to total amount of packet
-Lifetime : Evaluate the shortest lifetime of network
[1] P. Kindt, D. Yunge, M. Gopp and S. Chakraborty, “Adaptive online power-management for Bluetooth Low Energy”, IEEE Conference on Computer Communications (INFOCOM), 2015
[2] F. Shan, J. Luo, and X. Shen, “Optimal energy efficient packet scheduling with arbitrary individual deadline guarantee,” Compute. Netw., vol. 75, pp. 351–366, Dec. 2014
[3] Doudou, Messaoud, et al. "Duo-MAC: Energy and time constrained data delivery MAC protocol in wireless sensor networks." Wireless Communications and Mobile Computing Conference (IWCMC), 2013 9th International. IEEE, 2013.
[4] Jacob, Anil K., and Lillykutty Jacob. "Energy Efficient MAC for QoS Traffic in Wireless Body Area Network." International Journal of Distributed Sensor Networks 2015 .
[5] Collotta, Mario, Giovanni Pau, and Gianfranco Scatà. "Deadline-aware scheduling perspectives in industrial wireless networks: A comparison between IEEE 802.15. 4 and Bluetooth." International Journal of Distributed Sensor Networks 2013 (2013).
Notes: 簡介一下比較組

## Slide 18: Lifetime Model
●Node power model
Measuring Bluetooth® Low Energy Power Consumption
Parameter | Value | Description
Ia |  | Connection event current
Ta |  | Connection event duration
It |  | Average of rx and tx current
Tt |  | Duration of rx and tx current
Cbattery | 230mAh | The Battery Capacity
Vcoin | 3.3V | Battery Voltage
 |  | Connection event current
 |  | Connection event duration
 |  | Sleep current
 |  | Load of i th application
 |  | Maximum data byte of packet
pi |  | Period of i th application
HP |  | Hyper-period
Parameter | Value | Description
Ia |  | Connection event current
Ta |  | Connection event duration
It |  | Average of rx and tx current
Tt |  | Duration of rx and tx current
Cbattery | 230mAh | The Battery Capacity
Vcoin | 3.3V | Battery Voltage
 |  | Connection event current
 |  | Connection event duration
 |  | Sleep current
 |  | Load of i th application
 |  | Maximum data byte of packet
pi |  | Period of i th application
HP |  | Hyper-period

## Slide 19: Experiment (Service Interval)
● Single Node
(MEI, DIF, Lazy, and Greedy)
 Lazy proposes to gradually decrease the BLE rate by constant value and assign the highest rate to server application when the application rate is larger than BLE rate.
 DIF proposes to estimate the interval application rate and assign the BLE rate to every packet.
 Greedy would assign the minimum period as the connection interval.
Chart: Meet Ratio
| 80 | 120 | 160 | 200 | 240 | 280 | 320 | 360 | 400 | 440 | 480 | 520 | 560
DIF | 0.020709 | 0.060313 | 0.14834 | 0.11652 | 0.087587 | 0.050903 | 0.23038 | 0.064184 | 0.23459 | 0.054646
Lazy | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
MEI | 1 | 1 | 1 | 1 | 0.9997 | 0.99964 | 0.99971 | 0.99918 | 0.99956 | 0.99867
Greedy | 1 | 0.93735 | 0.85955 | 0.70943 | 0.51178 | 0.30245 | 0.20775 | 0.028433 | 0.066394 | 0.010034
Chart: Lifetime
| 80 | 120 | 160 | 200 | 240 | 280 | 320 | 360 | 400 | 440 | 480 | 520
DIF | 5059.04 | 2616.58 | 2242.63 | 1721.36 | 1868.9 | 1077.67 | 785.219 | 684.039 | 686.315 | 557.803
Lazy | 349.077 | 347.705 | 297.729 | 295.85 | 271.285 | 250.717 | 273.301 | 243.365 | 233.932 | 213.988
MEI | 1839.2 | 1405.85 | 1186.77 | 969.475 | 800.155 | 688.458 | 668.17 | 554.081 | 545.964 | 459.188
Greedy | 1844.23 | 1446.52 | 1273.81 | 1098.69 | 987.943 | 992.724 | 936.834 | 961.449 | 969.732 | 887.646
Notes: Meet ratio
Latency
Lifetime
DIF320, 480為(80bytes倍數)

## Slide 20: Experiment (Star Interval)
● Scaling Connection Interval
(EIMA, LDC, and Greedy)
 LDC proposes to use the low duty cycle to server the application and each interval would be divided by number of node to be the connection interval.
 Greedy proposes to let the minimum interval to be divided by number of node and assign as connection interval for every node.
Chart: Meet Ratio
| 80 | 120 | 160 | 200 | 240 | 280 | 320 | 360 | 400 | 440 | 480 | 520
MEI_EIMA_EIF | 0.89946 | 0.94854 | 0.9508 | 0.96049 | 0.98128 | 0.99001 | 0.99784 | 0.9932 | 0.98785 | 0.99594
MEI_LDC_EIF | 0.63651 | 0.8103 | 0.8241 | 0.8247 | 0.95875 | 0.94607 | 0.97413 | 0.98665 | 0.98311 | 0.98635
MEI_Greedy_EIF | 0.99892 | 0.99835 | 0.9987 | 0.99792 | 0.99614 | 0.99606 | 0.99868 | 0.99355 | 0.99323 | 0.99685
Chart: Lifetime
| 80 | 120 | 160 | 200 | 240 | 280 | 320 | 360 | 400 | 440 | 480 | 520
MEI_EIMA_EIF | 657.272 | 554.352 | 500.659 | 481.175 | 404.105 | 335.169 | 329.85 | 281.836 | 281.513 | 234.232
MEI_LDC_EIF | 426.641 | 409.12 | 401.546 | 373.998 | 343.073 | 290.844 | 296.411 | 250.952 | 252.277 | 208.87
MEI_Greedy_EIF | 423.793 | 391.954 | 377.019 | 359.243 | 328.684 | 279.368 | 280.114 | 242.928 | 243.247 | 202.675
Notes: Single node -> MEI
Mesh node -> TDMA, EIMA
Latency 為何會往下墜?
1.Input 中每一node的data rate相同，若時間越短 Load加重造成pkt數量不會有帶大的改變, 反之時間越常造成load變大, pkt數量顯而易見
2.

## Slide 21: Experiment (Write-Request Scheduler)
● Write-Request Schedule
(EIF, Polling, NPEDF, and Round Robin)
 NPEDF proposes to schedule as the Earliest Deadline First in non-preemptive.
 Polling proposes assign the schedule table by priority of node.
 Round Robin proposes assign the schedule table and assign each one time.
Chart: Meet Ratio
| 80 | 120 | 160 | 200 | 240 | 280 | 320 | 360 | 400 | 440 | 480 | 520
MEI_EIMA_EIF | 0.89946 | 0.94854 | 0.9508 | 0.96049 | 0.98128 | 0.99001 | 0.99784 | 0.9932 | 0.98785 | 0.99594
MEI_EIMA_NPEDF | 0.81767 | 0.89383 | 0.93856 | 0.93707 | 0.98121 | 0.98571 | 0.99784 | 0.9932 | 0.98785 | 0.99594
MEI_EIMA_Polling | 0.54797 | 0.5403 | 0.68951 | 0.65017 | 0.73872 | 0.81485 | 0.82228 | 0.82751 | 0.82889 | 0.81042
MEI_EIMA_Round Robin | 0.42032 | 0.48876 | 0.53191 | 0.51136 | 0.62643 | 0.75189 | 0.72715 | 0.81991 | 0.8334 | 0.87355
Chart: Lifetime
| 80 | 120 | 160 | 200 | 240 | 280 | 320 | 360 | 400 | 440 | 480 | 520
MEI_EIMA_EIF | 657.272 | 554.352 | 500.659 | 481.175 | 404.105 | 335.169 | 329.85 | 281.836 | 281.513 | 234.232
MEI_EIMA_NPEDF | 657.391 | 554.441 | 500.613 | 481.178 | 404.105 | 335.165 | 329.85 | 281.831 | 281.51 | 234.232
MEI_EIMA_Polling | 664.666 | 558.673 | 501.837 | 482.801 | 405.318 | 335.856 | 330.938 | 283.224 | 283.299 | 235.053
MEI_EIMA_Round Robin | 697.238 | 565.446 | 503.133 | 482.992 | 404.832 | 333.516 | 328.454 | 279.13 | 280.809 | 232.359
Notes: Single node -> MEI
Mesh node -> TDMA, EIMA

## Slide 22: Experiment (Varied Node Number)
● Node Number
(80bytes/s)
GGRR=Greedy Greedy Round Robin
Notes: Single node -> MEI
Mesh node -> TDMA, EIMA

## Slide 23: Experiment (Service Interval)
● Single Node
(MEI, DIF, Lazy, and Greedy)
 Lazy proposes to gradually decrease the BLE rate by constant value and assign the highest rate to server application when the application rate is larger than BLE rate.
 DIF proposes to estimate the interval application rate and assign the BLE rate to every packet.
 Greedy would assign the minimum period as the connection interval.
Chart: Meet Ratio
| 80 | 120 | 160 | 200 | 240 | 280 | 320 | 360 | 400 | 440 | 480 | 520 | 560
DIF | 0.020709 | 0.060313 | 0.14834 | 0.11652 | 0.087587 | 0.050903 | 0.23038 | 0.064184 | 0.23459 | 0.054646
Lazy | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
MEI | 1 | 1 | 1 | 1 | 0.9997 | 0.99964 | 0.99971 | 0.99918 | 0.99956 | 0.99867
Greedy | 1 | 0.93735 | 0.85955 | 0.70943 | 0.51178 | 0.30245 | 0.20775 | 0.028433 | 0.066394 | 0.010034
Chart: Lifetime
| 80 | 120 | 160 | 200 | 240 | 280 | 320 | 360 | 400 | 440 | 480 | 520
DIF | 5059.04 | 2616.58 | 2242.63 | 1721.36 | 1868.9 | 1077.67 | 785.219 | 684.039 | 686.315 | 557.803
Lazy | 349.077 | 347.705 | 297.729 | 295.85 | 271.285 | 250.717 | 273.301 | 243.365 | 233.932 | 213.988
MEI | 1839.2 | 1405.85 | 1186.77 | 969.475 | 800.155 | 688.458 | 668.17 | 554.081 | 545.964 | 459.188
Greedy | 1844.23 | 1446.52 | 1273.81 | 1098.69 | 987.943 | 992.724 | 936.834 | 961.449 | 969.732 | 887.646
Notes: Meet ratio
Latency
Lifetime
DIF320, 480為(80bytes倍數)

## Slide 24: Experiment (Star Interval)
● Scaling Connection Interval
(EIMA, LDC, and Greedy)
 LDC proposes to use the low duty cycle to server the application and each interval would be divided by number of node to be the connection interval.
 Greedy proposes to let the minimum interval to be divided by number of node and assign as connection interval for every node.
Chart: Meet Ratio
| 80 | 120 | 160 | 200 | 240 | 280 | 320 | 360 | 400 | 440 | 480 | 520
MEI_EIMA_EIF | 0.89946 | 0.94854 | 0.9508 | 0.96049 | 0.98128 | 0.99001 | 0.99784 | 0.9932 | 0.98785 | 0.99594
MEI_LDC_EIF | 0.63651 | 0.8103 | 0.8241 | 0.8247 | 0.95875 | 0.94607 | 0.97413 | 0.98665 | 0.98311 | 0.98635
MEI_Greedy_EIF | 0.99892 | 0.99835 | 0.9987 | 0.99792 | 0.99614 | 0.99606 | 0.99868 | 0.99355 | 0.99323 | 0.99685
Chart: Lifetime
| 80 | 120 | 160 | 200 | 240 | 280 | 320 | 360 | 400 | 440 | 480 | 520
MEI_EIMA_EIF | 657.272 | 554.352 | 500.659 | 481.175 | 404.105 | 335.169 | 329.85 | 281.836 | 281.513 | 234.232
MEI_LDC_EIF | 426.641 | 409.12 | 401.546 | 373.998 | 343.073 | 290.844 | 296.411 | 250.952 | 252.277 | 208.87
MEI_Greedy_EIF | 423.793 | 391.954 | 377.019 | 359.243 | 328.684 | 279.368 | 280.114 | 242.928 | 243.247 | 202.675
Notes: Single node -> MEI
Mesh node -> TDMA, EIMA
Latency 為何會往下墜?
1.Input 中每一node的data rate相同，若時間越短 Load加重造成pkt數量不會有帶大的改變, 反之時間越常造成load變大, pkt數量顯而易見
2.

## Slide 25: Experiment (Write-Request Scheduler)
● Write-Request Schedule
(EIF, Polling, NPEDF, and Round Robin)
 NPEDF proposes to schedule as the Earliest Deadline First in non-preemptive.
 Polling proposes assign the schedule table by priority of node.
 Round Robin proposes assign the schedule table and assign each one time.
Chart: Meet Ratio
| 80 | 120 | 160 | 200 | 240 | 280 | 320 | 360 | 400 | 440 | 480 | 520
MEI_EIMA_EIF | 0.89946 | 0.94854 | 0.9508 | 0.96049 | 0.98128 | 0.99001 | 0.99784 | 0.9932 | 0.98785 | 0.99594
MEI_EIMA_NPEDF | 0.81767 | 0.89383 | 0.93856 | 0.93707 | 0.98121 | 0.98571 | 0.99784 | 0.9932 | 0.98785 | 0.99594
MEI_EIMA_Polling | 0.54797 | 0.5403 | 0.68951 | 0.65017 | 0.73872 | 0.81485 | 0.82228 | 0.82751 | 0.82889 | 0.81042
MEI_EIMA_Round Robin | 0.42032 | 0.48876 | 0.53191 | 0.51136 | 0.62643 | 0.75189 | 0.72715 | 0.81991 | 0.8334 | 0.87355
Chart: Lifetime
| 80 | 120 | 160 | 200 | 240 | 280 | 320 | 360 | 400 | 440 | 480 | 520
MEI_EIMA_EIF | 657.272 | 554.352 | 500.659 | 481.175 | 404.105 | 335.169 | 329.85 | 281.836 | 281.513 | 234.232
MEI_EIMA_NPEDF | 657.391 | 554.441 | 500.613 | 481.178 | 404.105 | 335.165 | 329.85 | 281.831 | 281.51 | 234.232
MEI_EIMA_Polling | 664.666 | 558.673 | 501.837 | 482.801 | 405.318 | 335.856 | 330.938 | 283.224 | 283.299 | 235.053
MEI_EIMA_Round Robin | 697.238 | 565.446 | 503.133 | 482.992 | 404.832 | 333.516 | 328.454 | 279.13 | 280.809 | 232.359
Notes: Single node -> MEI
Mesh node -> TDMA, EIMA

## Slide 26: Experiment (Varied Node Number)
● Node Number
(80bytes/s)
Chart: Meet Ratio
| 3 | 4 | 5 | 6 | 7 | 8
MEI_EIMA_EIF | 0.89946 | 0.98293 | 0.99164 | 0.99421 | 0.99304 | 0.99535
Greedy_Greedy_Round Robin | 0.99961 | 1 | 1 | 0.99999 | 0.99992 | 1
Chart: Lifetime
| 3 | 4 | 5 | 6 | 7 | 8
MEI_EIMA_EIF | 657.272 | 426.927 | 373.491 | 353.417 | 281.974 | 258.271
Greedy_Greedy_Round Robin | 423.873 | 275.924 | 225.301 | 188.093 | 154.616 | 135.98
Notes: Single node -> MEI
Mesh node -> TDMA, EIMA

## Slide 27: Case Study
●Wireless Body Sensor Network
-Emergence scenario
-Real-time delivery
●Architecture
-Star topology with three slaves
http://www.ti.com/product/CC2540
CC2540/CC2541 | 
Device Type | Wireless MCU
Bluetooth Standard | Bluetooth Smart (Bluetooth low energy)
Flash size (KB) | 128 256
RAM size (KB) | 8
RX Current (Lowest) (mA) | 19.6
Standby Current (uA) | 0.4
Wakeup Time (PD-->RX/TX) (us) | 530
Sensitivity (Best) (dBm) | -93
Operating Temperature Range (C) | -40 to 85
Notes: Power function上的考量

## Slide 28: Case Study
●Implement
- GATTMsg Receive request message and Response
- Buffer Queue Manage sensing data
- Write-request schedule is controlled by the master.
OSAL
Peripheral
Profile
Application
GATTMsg
Buffer Queue
Host
GATT
Host Control Interface (HCI)
Controller
MEI
EIMA
EIF
Callback Function
HCI
BLE Stack
Notes: Buffer Queue若沒有BufferQueue會以各自service觸發notification
導致切換node時 packet loss
GATTMsg已我們的write-request方式，避免等待過長時間

## Slide 29: Experiment
● Setting
Input |  | Connection interval (EIMA) | Connection interval (Greedy)
Slave1 | Pkt1(8bytes, 200ms) Pkt2(8bytes, 200ms) | 100ms | 50ms
Slave2 | Pkt1(16bytes, 400ms) Pkt2(16bytes, 400ms) | 100ms | 50ms
Slave3 | Pkt1(20bytes, 800ms) Pkt2(20bytes, 800ms) | 100ms | 50ms

## Slide 30: Conclusion
●In the WSN, it is hard to balance the power consumption and latency of each sensor node with real-time and collision constraint.
●We propose MEI to determine the interval with varied data rate.
EIMA to extend the lifetime of network with collision constraint.
EIF to decrease the latency by defining device’s priority.
●In our simulation and practice, it is obviously to see our proposal has the better performance in meet ratio and high lifetime for the whole sensor network.

## Slide 31: Experiment
● Setting
Chart: Lifetime (Simulation)
| 40 | 80 | 120 | 160 | 200 | 240 | 280 | 320 | 360 | 400 | 440 | 480 | 520 | 560 | 600 | 640 | 680 | 720 | 760 | 800 | 840 | 880 | 920 | 960
MEI_EIMA_EIF (Is=1uA) | 673.877 | 657.272 | 554.352 | 500.659 | 481.175 | 404.105 | 335.169 | 329.85 | 281.836 | 281.513 | 234.232 | 239.845
MEI_EIMA_EIF (Is=400uA) | 364.329 | 366.289 | 342.615 | 332.463 | 318.902 | 295.367 | 256.062 | 256.777 | 225.697 | 225.839 | 190.993 | 198.309
Greedy_Greedy_Round Robin(Is=1uA) | 420.772 | 423.873 | 392.903 | 382.89 | 362.382 | 349.613 | 324.341 | 316.661 | 295.945 | 310.259 | 273.325 | 284.316
Greedy_Greedy_Round Robin(Is=400uA) | 252.496 | 253.44 | 243.66 | 240.041 | 232.908 | 227.992 | 216.642 | 213.666 | 203.423 | 209.536 | 192.368 | 197.201

## Slide 32: Experiment
● Setting
Chart: 
Chart: 

## Slide 33: Proposal (Write-Request Scheduler)
● Write-Request Schedule
-The write-request scheduler usually implements the table order to notify device.
● Earliest Interval First Schedule (EIF)
-The MEI define the urgent interval for each node, and assign as period of each node.
-The EIMA is estimated for device transmission duration for avoid collision problem.
- The scheduler proposes to decide whether the node (), not arrival would be blocking by other node ().
N1
N2
N3
GW
Frame1(N1)
Frame3(N3)
Frame2(N2)
Notes: 預測是否會被其他slave block

## Slide 34: Proposal (Star Interval)
● Energy Efficiency Interval Multiple Access (EIMA)
-It determine the waiting time for master to each node with avoiding collision.
-It can balance network energy consumption for each node to extend lifetime.
Parameter | Value | Description
 |  | Connection event current
 |  | Connection event duration
 |  | Sleep current
 |  | Service interval of i th node
 |  | Connection interval of i th node
Parameter | Value | Description
 |  | Connection event current
 |  | Connection event duration
 |  | Sleep current
 |  | Service interval of i th node
 |  | Connection interval of i th node
Consider to lifetime
Consider to each slave
Notes: 將current當為weight
考量彼此slave
U=1

## Slide 35: Node scheduler
● Property
Event-driven
● Issue
The interval between both events
is the critical point for energy efficiency.
Sleeping time can lower the current.
● Improve
Buffer assignment
BLE stack <Peripheral>
Pkt
Pkt
Pkt
…
Buffer
Notes: OSAL

## Slide 36: Discovery issue
● J. Liu et.al., ”Modeling and performance analysis of device discovery in Bluetooth Low Energy networks,” Proc. IEEE Global Commun. Conf., Anaheim, CA, USA, 2012, pp.1538-1543
● Jan Jaap Treurniet, Chayan Sarkar, R. Venkatesha Prasad, Willem de Boer “Energy Consumption and Latency in BLE Devices under Mutual Interference: An Experimental Study”, 2015
, if
Parameter | Description
Tproc,disc | Discovery processing time, affected by duty cycle of scan window
Nadv | Amount of advertisment device
Tscan_inter | Scan interval for switching listen channel
Tscan_win | Scan window for listensing chnnel
Tadv | Advertisement interval
● Discovery process /latency
-The response data, sent by advertising node should be only allowed for one pattern.
-Duty cycle of scan process effects the discovery time.
-The critical delay time is coming from the advertising interval (Ta).
Conn
Adv
Notes: Modeling and Performance Analysis of Device Discovery in Bluetooth Low Energy Networks
(雖然duty cycle對於delay time有影響，另一方面若duty cycle為1但scan window 帶過長，因LL曾是必須等到scan window 結束才會response ，因此時間也不可過長)

## Slide 37: Measure
Interval = 10ms
Interval = 2000ms

## Slide 38: Measure
Connection event
Advertisement event
Notes: 為何不全部用Advertisement?
因一event上會有額外的消耗 (37, 38 39)

## Slide 39: Measure
Single packet
Multiple packets
Scan
Notes: Power function上的考量

## Slide 40: BLE State
http://wiki.t-firefly.com/index.php/FireBLE/protocol_stack/en
http://e2e.ti.com/support/wireless_connectivity/bluetooth_low_energy/f/538/p/375805/1323302#1323302
● BLE State (Link Layer)
-The state of sequence packet transmission stays in connection.
-In multiple notification issue, if two slaves response data to master, the buffer would be erased by the later arrival one.
Notes: Initial->Device waits to receive advertising packet from a specific device, and responds with connection request
Connection->Device exchanges data
Standby-> sleep
1.連傳機制會以現在的packet priority最高
導致其他node collision
2.若沒有BufferQueue會以各自service觸發notification
導致切換node時 packet loss
Adv > Conn
若有Adv node則為去監聽，之後再切回Conn (Buffer)

## Slide 41: Mesh Network
● Gateway (Central)
-It controls the write-request schedule and receives the sensing data.
● Conn Node (Peripheral and Observer)
-The sensor node is connecting to the gateway and scanning the date form the Adv node.
● Adv Node (Broadcaster)
-The sensor node is playing as advertising role and being as beacon, for broadcasting event.
● Mesh
-To establish sensor network for wide range, it allow the device to communicate to each others.
http://ble-mesh.com/
Notes: 與lifetime equ串連

## Slide 42: Proposal (Star Interval)
● Energy Efficiency Interval Multiple Access (EIMA)
.
Parameter | Value | Description
 |  | Connection event current
 |  | Connection event duration
 |  | Sleep current
 |  | Connection interval of i th node
Parameter | Value | Description
 |  | Connection event current
 |  | Connection event duration
 |  | Sleep current
 |  | Connection interval of i th node
Notes: 解碰撞 以及extend lifetime

## Slide 43: Mesh Solution
●Lifetime and Latency
- The interval in Adv Node would cause the discovery latency and energy consumption in Conn Node and Adv Node.
-We propose to make the power consumption of Conn node same as that of Adv node.
● J. Liu et.al., ”Modeling and performance analysis of device discovery in Bluetooth Low Energy networks,” Proc. IEEE Global Commun. Conf., Anaheim, CA, USA, 2012, pp.1538-1543
● Jan Jaap Treurniet, Chayan Sarkar, R. Venkatesha Prasad, Willem de Boer “Energy Consumption and Latency in BLE Devices under Mutual Interference: An Experimental Study”, 2015
Conn
Adv
Energy
Energy
Parameter | Description
Tproc,disc | Discovery processing time, affected by duty cycle of scan window
Nadv | Amount of advertisment device
Tscan_inter | Scan interval for switching listen channel
Tscan_win | Scan window for listensing chnnel
Tadv | Advertisement interval
Notes: 簡介一下比較組

## Slide 44: Process Power
●Process power
Measuring Bluetooth® Low Energy Power Consumption
Chart: 
Chart: Without Process
217Hours
235Hours

## Slide 45: Power & Lifetime Model
●Node power model
Measuring Bluetooth® Low Energy Power Consumption
Parameter | Value | Description
Ia |  | Connection event current
Ta |  | Connection event duration
It |  | Average of rx and tx current
Tt |  | Duration of rx and tx current
Cbattery | 230mAh | The Battery Capacity
Vcoin | 3.3V | Battery Voltage
 |  | Connection event current
 |  | Connection event duration
 |  | Sleep current
 |  | Load of i th application
 |  | Maximum data byte of packet
pi |  | Period of i th application
HP |  | Hyper-period
Parameter | Value | Description
Ia |  | Connection event current
Ta |  | Connection event duration
It |  | Average of rx and tx current
Tt |  | Duration of rx and tx current
Cbattery | 230mAh | The Battery Capacity
Vcoin | 3.3V | Battery Voltage
 |  | Connection event current
 |  | Connection event duration
 |  | Sleep current
 |  | Load of i th application
 |  | Maximum data byte of packet
pi |  | Period of i th application
HP |  | Hyper-period